## Slide 1: Incorporating 61968-13 into 61970-45x
13 June 2023

## Slide 2: Topics
61970-45x and 61968-13: The lay of the land
Why the existing picture is not optimal
Why we profile
How we profile
What could/should we do
Next steps

## Slide 3: 61970-45x and 61968-13: The lay of the land
We have 2 sets of profiles which describe subsets of the grid model portion of the CIM
  One set was designed with transmission in mind, the other with a distribution perspective
  They use the same approach (non-overlapping profiles, a single base profile)
  This situation has resulted from the change in scope of WG13/14 from T/D to grid / support
  Unfortunately the two profiles now describe different subsets of the underlying CIM information model (and one has lots of inconsistencies)

## Slide 4: 61970-45x and 61968-13: The lay of the land
Major differences
  One represents the grid in a balanced fashion, the other represents it in an unbalanced manner
    Which means there is/are
      Duplication of classes, attributes and associations describing basic equipment, connectivity and containment
      Additional phase-related classes in 61968-13
      Different modelling of ratings and impedances

## Slide 5: 61970-45x and 61968-13: The lay of the land
unbalanced
balanced
duplicated
not used

## Slide 6: 61970-45x and 61968-13: The lay of the land
Major differences
  One was developed with transmission application integration in mind, the other with distribution data exchanges in mind
    This means that consuming applications had differing data requirements which led to the different dividing lines between profiles

## Slide 7: 61970-45x and 61968-13: The lay of the land

## Slide 8: Why the existing picture is not optimal
Double maintenance for UCAIug TF/IEC WG – errors, inconsistencies, extra effort, extra time
Confusion and complexity for utilities
  Distribution utilities are often responsible for subtransmission (and use balanced power flow tools) in addition to lower voltage networks (where they use unbalanced tools))
  Data exchange across T and D is becoming a ubiquitous industry requirement (and some tool on one side or the other, needs to translate between balanced and unbalanced)
Messaging to industry (and education/training) is unnecessarily complex - it makes an already difficult ‘sales job’ much more difficult
Double work for vendors in interface development

## Slide 9: Why do we profile?
To define the structure and meaning of a bounded set of information that is shared
For a given instance of exchanged data, a profile:
  Supports validation of the defined set
  Doesn’t say anything about information outside the defined set
  Doesn’t require that objects of the defined set exist (other than by required associations)
When we define a standard profile, we are trying to enable interoperability
  We talk about tool interfaces that ‘conform’ to a standard profile (and we talk about conformity certification)
  There is an implication that the defined set of data can be read, validated and used as appropriate (“as appropriate” is fuzzy – if a tool clearly doesn’t use a particular type of data within the defined set, what does it need to do to conform?)

## Slide 10: How do we profile?
In two parts
  RDFS – provide the capabilities discussed above, easy to ‘see’ particularly when expressed in UML
  Constraints – provide finer grained profile definition, support more detailed validation, currently very difficult to ‘see’ and maintain
    Valid value ranges
    Instance requirements
    Complex cross-attribute, cross-class requirements relating to values, presence, number

## Slide 11: Where do we go?
Can we define an approach that
  Defines profiles that reflect consuming application needs across both T & D
  Streamlines modelling and maintenance of balanced and unbalanced profiles

## Slide 12: Profile divisions to meet consuming application needs
Our 61970-45x and 61968-13 profiles both ‘subdivide’ Physical grid model data into profiles by type of consumer

## Slide 13: Profile divisions to meet consuming application needs

## Slide 14: Model streamlining to support balanced and unbalanced
+ lengthFromTerminal [0..1]
+ normalOpen
ConductingEquipment
ProtectedSwitch
EQ
base profile

## Slide 15: Model streamlining to support balanced and unbalanced
+ ratedCurrent [0..1]
+ retained
ConductingEquipment
balanced EQ adder profile
ProtectedSwitch
Breaker

## Slide 16: Model streamlining to support balanced and unbalanced
+ switchOnCount [0..1]
+ switchOnDate [0..1]
unbalanced EQ adder profile
+ closed [0..1]
+ normalOpen [0..1]
+ phaseSide1 [0..1]
+ phaseSide2 [0..1]
Notes:
Switch.ratedCurrent is in ElectricalProperties profile
Switch.switchOnCount is <<deprecated>>in canonical UML
Switch.switchOnDate is <<deprecated>>in canonical UML
SwitchPhase.closed is erroneously in Functional
SwitchPhase.ratedCurrent is in ElectricalProperties

## Slide 17: Agreement for moving forward
Have official, visible profiles for instance exchange (expressed in rdfs) – Physical, Situation, Solution, Asset, Asset Catalog, GeographicalLocation, DiagramLayout 1,2
The Physical, Situation and Solution profiles are made up of sub-profiles that are managed as such in profiling tools (and have independent maintenance & versioning) and have independent sets of constraints defined.
Individual exchanges and vendor conformity can be specified at the sub-profile level.
1- acknowledge that the tank-based transformer modelling needs to be clarified to work in alignment with this
2- current proposal has only 4 rdfs level profiles – Physical, Situation, Solution, Diagram Layout

## Slide 18: Agreement for moving forward
Standard numbering:
  452 – Physical – Connectivity, non-Short Circuit & Short Circuit Electrical Parameters
  456 – Situation and Solution
  457 – Physical - Dynamics
  453 – Diagram Layout
  ?add to 452? - Asset
  ?add to 452? - Asset Catalogue
  ?add to 452? – Geographical Location

## Slide 19: Agreement for moving forward
 | Base | balanced | unbalanced
Solution (TP + SV) |  | x | x
Situation (SSH renamed) |  | x | x
Physical - dynamics |  |  | 
Physical - measurement |  |  | 
Physical - short circuit | x | x | to be checked
Physical - electrical | x | x | x
Physical - connectivity | x | x | x
Asset Catalog |  |  | 
Asset |  |  | 
DiagramLayout (DL) |  |  | 
GeographicalLocation (GL) |  |  | 

## Slide 20: Agreement for moving forward – current proposal