## Slide 1: IEC TC57/WG10 Report on units in IEC 61850
Thierry Dufaure February 26th, 2025

## Slide 2: Agenda
Current usage of « units » in different IEC 61850 documents
Data Object extension rules

## Slide 3: Definition of unit in IEC 61850-7-3 Enumeration
SIUnitKind – enumeration
Are extensions of SIUnitKind enumeration allowed?
  Negative range by private namespace Y – restriction: not for expressing standardized unit : MV (multiplier = 6, SIUnit = V).
  Positive range by TS/PAS – Y

## Slide 4: Definition of unit in IEC 61850-7-3 Enumeration
MultiplierKind – enumeration (m, k, M, …)
Are extensions of MultiplierKind enumeration allowed?
  Negative range already used by standard namespace
  Definition of multiplier component should always be understood as 10exp(value).

## Slide 5: Definition of Constructed Attribute Class Unit in IEC 61850-7-3
IEC 61850-7-3 defines the Constructed Attribute Class Unit, specifying a default value for multiplier
Default multiplier: « » = 10^0

## Slide 6: Instantiation of Data Attribute « units » in IEC 61850-7-3
Data Attribute « units » of type « Unit » is defined in the following CDCs:
  INS, INC, ING (introduced in IEC 61850 Edition 2)
  BCR
  HST
  MV, CMV, SAV
  APC, BAC, ASG
Note: CDC: CSG, CSD are using several DataAttribute xUnits, yUnits, zUnits
Note: The component Vector.ang is specified with a fixed non exposed units: {multiplier « », deg} within a fixed range = [-180, 180]

## Slide 7: Usage of unit in IEC 61850-7-4
There are Data Object names mandating their unit:
Abbreviation
Note: In IEC 61850-7-3 Edition 1 there was no Data Attribute « units » for INS, INC, ING: it made sense to mandate the unit in the Data Object name.

## Slide 8: Usage of Units in IEC 61850-7-4
There are Data Object explanations indicating their unit:

## Slide 9: Usage of Units in IEC 61850-7-4
There are Data Object explanation indicating their typical units:
SIUnit « K » kelvin: Temperature
Derived SIUnit « °C » degrees Celsius: Relative Temperature
Typically is used for typical usage.
There are Data Object without any units indication (for instance DO Pres [MV] vs Tmp[MV])

## Slide 10: Usage of Units in IEC 61869-9
Product standard may force the unit of a Data Object as well as other configuration aspects

## Slide 11: Usage of Units in IEC 61850-7-420
There are Data Object explanations indicating the different possible interpretations of a Data Object i.e. allowing different units (absolute or percentage)

## Slide 12: Usage of Units in IEC 61850-7-420
There are exclusive Data Objects to select the adequate representation art (absolute or percentage)

## Slide 13: IEC 61850-1-2 Data Object naming rules involving unit
General naming rule:
Mandate the unit in the the Data Object name if not SI

## Slide 14: IEC 61850-1-2 Data Object extension rules involving unit
Note: there are always exception to a rule: RFLO.FltDiskm [MV] exits since IEC 61850-7-4 Edition 1

## Slide 15: Recommendation
Optional Data Attributes should be used on a best effort basis and not as “as long it is not mandatory, I do not implement it”
Always prefer the self-descriptive model approach to avoid ambiguity

## Slide 16: Next steps
Shall we include a unit property in the UML model, and expose it in the NSD?
Note it may be tricky when the « units » is context sensitive:
Shall we make the Data Attribute « units » mandatory in IEC 61850-7-3 Edition 3?
Notes: How to get access to the papers?
-> E-mail sent on 16th of August to Christoph Brunner for CIGRE WG and IEEE to get access. IEEE papers should be listed.
-> Arun will check for PSRC
Thierry Coste have some additional papers to share.

## Slide 17: WG10 Conclusion – Delft Meeting
Continue discussion within TF UML and Autogeneration.
Consider exposing the fixed, typical, and optional units in the UML model and in the NSD for a machine processable exposure.
Notes: How to get access to the papers?
-> E-mail sent on 16th of August to Christoph Brunner for CIGRE WG and IEEE to get access. IEEE papers should be listed.
-> Arun will check for PSRC
Thierry Coste have some additional papers to share.

## Slide 18: Unit properties in Word Document
How should unit property be exported in the Word Document?
Proposal
DO without unit
DO with fixed unit
DO with fixed SIUnit

## Slide 19: Unit properties in Word Document
How should unit property be exported in the Word Document?
Proposal
DO with fixed non unit
DO with multiple SIUnit

## Slide 20: Unit properties in NSD
How should unit property be exported in the nsd?
Proposal

## Slide 21: Unit Property in UML
How to specify the unit property in UML?
Proposal as constraints of the DO instance

## Slide 22: AHTF Conclusion – Fribourg meeting
Exposing the fixed, typical, and optional units in the UML model, in the NSD and in Word document for a machine processable exposure. But first after Edition 2025.
In 1-2 revision – Description text shall expose the units restriction; the DOName shall be unit agnostic
Approval process for SIUnitKind similar to the abbreviation approval process. SIUnitKind extension approval done inside the TF UML and Autogeneration
Notes: How to get access to the papers?
-> E-mail sent on 16th of August to Christoph Brunner for CIGRE WG and IEEE to get access. IEEE papers should be listed.
-> Arun will check for PSRC
Thierry Coste have some additional papers to share.

## Slide 23: AHTF Conclusion – Fribourg meeting
Negative extension of SIUnitKind restricted to none existing units
Extension of MultplierKind restricted to the 10exp(ord) definition.
IEC 61850-8-1 fixed length GOOSE encoding for enumeration will need to define an escape value for enumeration values bigger than the 8-bit allowed range. Tissue expected to solve the issue.
Notes: How to get access to the papers?
-> E-mail sent on 16th of August to Christoph Brunner for CIGRE WG and IEEE to get access. IEEE papers should be listed.
-> Arun will check for PSRC
Thierry Coste have some additional papers to share.

## Slide 24
www.iec.ch